## Slide 1
License plate recognition based on target detection and semantic
曾子涵
Intelligent control technology

## Slide 2
Why choose this topic
License plate location based on target detection
License plate cutting and tilt correction
License plate character recognition
1
2
4
5
CONTENTS
License plate location based on semantic segmentation
3
Summary
6

## Slide 3
01
Why choose this topic
When you search for license plate recognition on Baidu, almost all methods use traditional image processing technologies, such as color feature analysis, edge detection technology and so on.
Moreover, there is almost no open-source license plate data on the network, resulting in almost all tutorials can not be used directly. Therefore, I hope to try some new methods through the open source data I can find.
edge detection

## Slide 4
01
Realization idea
Tilt correction
License plate location
Character recognition
Object detection?
Correct after finding four vertices
Single character recognition or recognition together

## Slide 5
02
Target detection algorithm ---- Fast RCNN
600*80038 * 50 characteristic layer  RPN regional recommendation network

## Slide 6
02
Target detection algorithm ---- Fast RCNN
ROI pooling  Classification and regression

## Slide 7
02
Target detection algorithm ---- Data preprocessing
CCPD dataset of China University of science and technology
https://github.com/detectRecog/CCPD
·The license plate location information is marked in the photo name
·I chose CCPD_ Base's 10000 photos for training

## Slide 8
02
Target detection algorithm ---- Data preprocessing
There is no annotation file in the CCPD dataset, so I wrote a code to parse the photo name and generate an XML annotation file

## Slide 9
02
Target detection algorithm ---- network structure
Backbone feature extraction network (resnet50)
RPN recommended network
Roipooling layer

## Slide 10
02
Target detection algorithm ---- Training results
This network is very time-consuming. After running on my classmate’s RTX 3060ti for a day and a night, I got a model with a loss of 0.0691 in the training set and 0.0675 in the verification set

## Slide 11
02
Target detection algorithm ---- run into a stone wall
My initial idea was to obtain the approximate location of the license plate through target detection, and then obtain the four vertices of the license plate through edge detection. However, for the license plate with too large tilt angle, it will cause a lot of interference and it is difficult to locate the vertex

## Slide 12
03
Semantic segmentation algorithm
If the target detection algorithm can tell us that there is a car and a person in the left picture, the semantic segmentation algorithm can accurately tell us which pixel in the picture is a car and which pixel is a person.
General process:

## Slide 13
03
Semantic segmentation algorithm ---- Data preprocessing
In order to obtain the pixel information of the license plate position, I modified the previous analysis code and marked the pixel value corresponding to the license plate as 255. The final effect is as follows.

## Slide 14
03
Semantic segmentation algorithm ---- network structure
UNET network structure

## Slide 15
03
Semantic segmentation algorithm ---- Training results
input
output

## Slide 16
04
License plate corner extraction
In order to obtain corner information in the experiment, my first idea is to use cv2.boundingRect to obtains the minimum circumscribed rectangle of the license plate. At this time, you can imagine that the rectangle is composed of four parts. Start from the vertex of each part and look outside for whether there is an intersection. The final results are as follows:

## Slide 17
04
Tilt correction

## Slide 18
05
Character recognition ---- Network construction

## Slide 19
05
Character recognition ---- Data preprocessing
The real difficulty of license plate recognition is the search of data. In the previous process of license plate recognition, I used the open-source data set of China University of science and technology. Although this data set contains the information of license plates, there is a big problem, that is, because the collection place is from Hefei, almost all license plates are from Anhui a, which makes this data set almost unavailable. There is little information about the data set of the whole license plate on the Internet.
Fortunately, I found an open source project to forge Chinese license plates on the Internet（ https://github.com/ufownl/fake_chs_lp ）, you can output any license plate. The blue cards generated are as follows:

## Slide 20
05
Character recognition ---- Data preprocessing
So I generated 2000 random license plate information for training, as shown in the figure below. The license plate information is saved in the form of file name.

## Slide 21
05
Character recognition ---- Data preprocessing
My initial idea was to use these 2000 random license plates to train the license plate recognition network, but after 100 rounds of iteration, I soon found the problem: the trained network has a high accuracy for identifying the same forged license plate, but it is almost impossible to recognize the real license plate.
After analyzing the reasons, I think the reason for this problem is that the 2000 license plates are too regular: the information of each license plate is very clear, and the location is very accurate, resulting in an almost unrecognizable phenomenon.
In order to solve this problem, I decided to enhance the data of these 2000 photos. I randomly rotate and translate these 2000 photos, add some noise to them, and blur them randomly. Finally, in order to eliminate the influence of color difference on judgment, I also binarized these 2000 pictures. The final effect pictures are as follows:

## Slide 22
05
Character recognition ---- Data preprocessing

## Slide 23
05
Character recognition ---- Training and testing

## Slide 24
06
Final effect
input
Output of Unet
Corner extraction
Tilt correction
Character recognition

## Slide 25
THANKS!
Intelligent control technology

## Slide 26
02
Target detection algorithm ---- Fast RCNN